## Slide 1: Video capabilities, minimum benchmark standards and best practices for in call treatment
2015

## Slide 2: General Considerations
  Environmental best practices – including:
    position lighting,
    reduced movement,
    neutral clothing & backgrounds
  Code in Network Quality Indicators which indicate packet loss in network
  Implement Quality of Service within own network. Control what you can. For example: prioritize traffic leaving corporate network and entering internet.
  Conduct network assessment for network fitness for real time media
  Experience will only be as good as weakest link in the end-to-end network. Typically for B2C this will be ‘last mile’ leg to consumers

## Slide 3
The Key Factors affecting video/audio quality
Three factors influence the video/audio quality:
  Limitations on the device and what it will support
    Physical resolution of the camera, Graphics Processing Power, CPU, and resource contention by other application features and other applications running in the background.
    E.g. an iPad Air has the processing power to support higher resolutions than an iPad 2
    iPad2 has known WiFi performance characteristics at various iOS version levels
  Network Conditions
    QoS
    Available Bandwidth
    WiFi Spectrum Saturation
    Packet Loss
    Latency
  The resilience of the codec to the network conditions
    Solution supports NACK/PLI for the video stream which greatly improves resilience to packet loss allowing for a higher quality video experience even in poor network conditions.
    However, even this has limitations and logic needs to be employed to address higher thresholds of network problems.
Production Video Quality cannot be achieved without addressing the configuration of the network to support a quality video experience.
Production Video Quality cannot be achieved without analyzing resource consumption of client devices to ensure enough resources are available to achieve a positive end-user experience. Other background applications can easily effect resource availability.

## Slide 4
Supported Resolutions
 | Device Type |  |  |  |  | 
Resolution |  | iPad2 | iPad3 | iPad4 | iPad Air | Browser
 | CIF (352 x 288) @ 20fps | 58% 44MB | 55% 36MB | 38% 39MB | 22% 32MB | 
 | VGA (640x480) @ 30fps |  |  | 62% 44MB | 34% 90MB | 
 | 1280x720 @ 30fps |  |  |  | 55% 100MB | (1)
(1) Support for HD video depends on the supported resolutions on the webcam
Supported
Sometimes supported
Not supported
Values for iOS devices are CPU (average across all cores) and memory usage.

## Slide 5
Network Requirements
 | Required Bandwidth
CIF (352 x 288) @ 20fps | 300Kb/s
VGA (640x480) @ 30fps | 600Kb/s
1280x720 @ 30fps | 1.2Mb/s
The table below shows the bandwidth requirements against resolution and frame rate
  The values are independent of device type and apply to both inbound and outbound streams
  The values are based on ‘talking head’ view. Greater movement will result in reduced quality for a fixed bandwidth
In addition the following constraints exist for an acceptable experience:
  Packet loss:
    Video – no more than 20% loss
    Audio – no more than 10% loss
  Latency
    Latency won’t affect the quality but will affect the user experience if it is too high. We recommend no more than 100ms latency between the endpoint and Media Broker.
  Jitter
    Solution uses an adaptive jitter buffer that can grow to a 900ms maximum
    For best results jitter should be kept below 150ms
In all cases the audio takes approximately 90 Kb/s of this total (based on G711)

## Slide 6
Example on bandwidth usage
This table shows the effect of constrained bandwidth on audio/video quality:
Total Available Bandwidth (Kb/s) | iPad Audio | iPad Video | EX90 Audio | EX90 Video
2048 | Excellent | Excellent | Excellent | Excellent
1024 | Excellent | Good | Excellent | Excellent
800 | Excellent | Occasional compression artefacts that correct quickly | Excellent | Excellent
600 | Excellent | Occasional compression artefacts that correct quickly | Audio corrupts for 5-10s, then resumes | Blocks of 5-10s corruption then corrects
512 | Good | Choppy Video | Corrupted Audio | Occasional Image then corruption
256 | Very Choppy Distorted Audio | Very Choppy Video | Corrupted Audio | Corrupted Video
128 | Very Choppy Distorted Audio | Very Choppy Video | No Audio | No Video
64 | Corrupted Audio | One Static Image | No Audio | No Video
The scenario used an iPad 2 connected to a Wireless Access Point connected to a traffic shaping server. This allowed the total bandwidth into and out of the iPad to be constrained as per the first column.
Calls made using the CafeX sample app to a Cisco EX90 via CUCM streaming at 640x480 in both directions with the iPad using VP8 and MB transcoding to H264 for the EX90.
The leg from iPad to MB had a target bit rate of 512Kb/s for video and the audio used ~90Kb/s so requiring a total of 600Kb/s in each direction, or 1200Kb/s in total.
The table shows that when 1024Kb/s is available the user will experience good/excellent audio and video. At around 1200Kb/s it would be excellent across the board. The quality was acceptable as low as 800Kb/s.

## Slide 7
Decision Tree
 | Device Type |  |  |  |  | 
Bandwidth (Kb/s) |  | iPad2 | iPad3 | iPad4 | iPad Air | Browser
 | <90 | No call possible |  |  |  | 
 | 90-299 | Audio Only | Audio Only | Audio Only | Audio Only | Audio Only
 | 300-599 | 352x288@20fps | 352x288@20fps | 640x480@30fps | 640x480@30fps | 640x480@30fps
 | 600-1199 | 352x288@20fps | 352x288@20fps | 640x480@30fps | 640x480@30fps | 640x480@30fps
 | 1200+ | 352x288@20fps | 352x288@20fps | 640x480@30fps | 1280x720@30fps | 1280x720@30fps
Before the call
Determine the column for your particular device in the table above.
Use the bandwidth estimation utility to determine the available bandwidth.
Use the call settings for that bandwidth and device combination and make the call (if possible).
During the call
The network status callbacks will inform you of the quality of the network. Use this information to:
Possibly give visual feedback to the user about network quality.
If the quality of the network is poor then mute the video stream to allow the bandwidth to be used to improve the audio quality.
If the audio quality is still not acceptable then it should be a decision for the parties to that call as to whether they should end the call.

## Slide 8: Front-facing Camera Resolutions (2014)
Laptops |  | Tablets |  | Phones | 
Acer C720 ChromeBook | 1280x720 | iPad Air | 1280x960 | iPhone5s | 1280x960
Lenovo T440s | 1280x720 | iPad Mini | 1280x960 | iPhone5 | 1280x960
13” MacBook Air | 1280x720 | iPad2 | 640x480 VGA | iPhone 4S | 640x480 VGA
HP Spectre x2 (HP TrueVision HD Webcam) | 1280x1024 | Google Nexus 10 | 1600x1200 | Samsung Galaxy S4 | 1600x1200
Dell Inspiron 15 | 1280x1024 | Samsung Galaxy Note 10.1 | 1600x1200 | Samsung Galaxy Note 3 | 1600x1200
 |  |  |  | HTC One | 1600x1200